December 28, 2009

The Fuel, Emissions and Logistics group on behalf of American Electric Power Service Corporation, as agent for Ohio Power Company (“OPCo”) is seeking proposals for the supply of coal to one or more power plants.  OPCo may enter into one or more spot agreements, each for the supply of between 10,000 and 60,000 tons of coal per month, delivered by rail or barge, commencing as early as January 2010.

The solicitation seeks coal that meets the specifications on the attached “Coal Specification Table.”  All proposals will have specifically negotiated terms and conditions, but will mirror those included in this solicitation as close as practicable.

OPCo is seeking a proposal that provides for spot coal beginning as early as January 2010, and extending up to six months.

Each valid proposal should include:

- The Seller’s and Producer’s name(s)

- The location of the mine

- The mine type (surface or underground)

- The seam of coal being mined

- The mine district

- The quality of the coal, inclusive of suspension/rejection limits

- The coal preparation (washed, crushed run-of-mine, etc.)

- The tons proposed for delivery each month

- The stated price per ton

- The commencement date and months of delivery

Proposals for rail-delivered coal will require the rail origin station, the OPSL number, the number of railcars per shipment, the maximum loadout time, and the station’s ability to apply freeze control agents and what those agents would be.

The proposal(s) should include a stated price or prices (inclusive of all known or unknown costs associated with existing laws or government impositions) for the relevant term of the proposal(s).

A "Coal Proposal Form" and a "Rail Transportation Facilities Information" sheet, if applicable, or a "Barge Transportation Facilities Information" sheet, if applicable, shall comprise a Coal Proposal Package.  Copies of these forms are contained herein.  In order to ensure that proposals are responsive to OPCo's needs and provide a uniform basis for evaluation, those providing offers are requested to complete a Coal Proposal Package for each submitted offer.  Typical coal analyses, including the Proximate, Ultimate, Trace Element and Mineral Ash Analyses, Grindability Index, and Ash Fusion Temperatures, should be submitted with the attached Coal Proposal Package.

The Coal Proposal Package(s), signed by a person having proper authority to legally obligate the offering company, along with any additional supporting material, must be received no later than 5:00 p.m., Wednesday, January 6, 2010.   Proposals are to be kept open for OPCo's acceptance until 5:00 p.m., Wednesday, January 13, 2010.  All proposals are to be submitted by e-mail to coalrfp@aep.com, or by fax to (614) 583-1619 (Attention: Jason Rusk), or delivered in an envelope marked "OPCo RFP - LOW SULFUR PROPOSAL" and are to be addressed as follows:

OPCo RFP – LOW SULFUR PROPOSAL

ATTN:  JASON RUSK, MANAGER EASTERN FUEL PROCUREMENT

AMERICAN ELECTRIC POWER SERVICE CORP.

155 W. NATIONWIDE BLVD.

SUITE 500

COLUMBUS, OH  43215

Proposals will be evaluated based upon the following factors:

- Delivered cost (cents per million Btu)

- Coal quality with appropriate price adjustments for guaranteed percent ash and pounds SO2 per million Btu based on the relevant SO2 emissions allowances, inclusive of rejection limits.

- Reliability of supply and transportation flexibility

- Terms and conditions

OPCo reserves the right to modify or withdraw this invitation, to reject any or all proposals, and to terminate any subsequent negotiations at any time.  OPCo also reserves the right to accept one or more proposal(s) for a portion or for all of the quantities of coal it seeks to acquire with this invitation.

OPCo will consider every submitted offer on a confidential basis.

Those submitting proposals shall be responsible for the completeness and accuracy of all information contained in and used in preparation of its proposal(s) and for having supplied all necessary information.

If you do not wish to submit a proposal in response to this solicitation, please complete and return the attached "Decline To Offer" form on or before January 6, 2010.

Should further information be required, please contact Jason Rusk by telephone at (614) 583-6275.

Very truly yours,

James D. Henry

Vice President – Eastern Fuel Procurement

On behalf of American Electric Power Service Corporation

As agent for Ohio Power Company

### COAL SPECIFICATION TABLE

Specification  (Mitchell 1&2, CSX Rail and Barge)

As Received	Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	 12,300	12,000	<11,900

Sulfur Dioxide (lbs SO2./MMBtu)	 <2.10	  2.30		>2.50

Ash (%)	 12.00	  13.00	>14.00

Moisture (%)	   8.00              10.00                          >10.00

Volatile Matter (%)	 30.00	  N/A		<29.00

Grindability	 48.00	  N/A		<44.00

Ash Fusion Temp. (H=1/2W)	  2700	  N/A		<2600

Ohio Power Company 	     	                 Spot Proposal

155 W.  Nationwide Blvd. 												      					                                                                                                                     Page 1 of 2

Suite 500

Columbus OH 43215

(614) 583-6275

COAL PROPOSAL FORM

DATE:

To: 	OPCo RFP – LOW SULFUR PROPOSAL

JASON RUSK – MANAGER, EASTERN FUEL PROCUREMENT

AMERICAN ELECTRIC POWER SERVICE CORP

155 W.  NATIONWIDE BLVD.

SUITE 500

COLUMBUS OH  43215

Details concerning the supply of coal being offered herein to the Ohio Power Company (OPCo) are provided below:

1.	Seller(s):  (If Seller is a Sales Agent, include full names, addresses, and telephone numbers of Sales Agent and Producer and attach Producer's signed authorization for Sales Agent to “exclusively” make an offer on behalf of Producer.)

(a)  Seller(s):	(b)  Producer(s):

_____________________________________		____________________________________

_____________________________________ 	____________________________________

_____________________________________	____________________________________

_____________________________________ 	____________________________________

2.  Name(s) and location(s) of mine(s):  (Include name of mine operating company).

3.  Quantity offered (tons per month): _______________________________________________________________

4.  Term:  Up to 6 months (beginning January 2010); actual length of term shall be designated by OPCo in the event of its acceptance.  Seller is to specify the earliest month coal is available:

_________________________________________________________________________________________

5.  Shipping Point(s):

Rail Deliveries					Barge Deliveries

Origin Station:  								  	Shipping Point:

OPSL No. (Defined in OPSL 6000R):  		River:

No. of railcars/shipment* (>15): 		 	Milepost:

Maximum Loadout Time:   24 hrs. 	4 hrs. 

*The minimum size unit train is 90 railcars.

6.  Price: __________ $/ton.

COAL PROPOSAL FORM

Spot Proposal

Page 2 of 2

7.	Guaranteed coal specifications “As-Received”:

Contracted	Half Month Suspension**     Daily/Lot Suspension***								 Quarterly 	 Half-Month  		   Minimum/Maximum***

a)  Calorific Value (Btu per pound)    		___________ 	_____________		      ______________ Minimum

b)  Total Moisture (%)                  		___________        _____________         	      ______________ Maximum

c)  Ash (%)*                            		___________        _____________                     ______________ Maximum

d)  Volatile Matter (%)                 		___________        _____________                     ______________ Minimum

e)  Grindability (Hardgrove Index)       	___________        _____________                     ______________ Minimum

f)  Ash Fusion Temperature (H = 1/2 W), oF

in Reducing Atmosphere	         		___________        _____________                     ______________ Minimum

g)  Sulfur (%)                           		___________        _____________                     ______________ Maximum

h)  SO2 (lbs./MMBtu) *             		___________        _____________                     ______________ Maximum

i)  Chlorine Dry (%)				___________        _____________                     ______________ Maximum

j)  Sodium Dry (%)				___________        _____________                     ______________ Maximum

k) Coal Top Size    	                 								      ______________

*	Offer evaluations will include appropriate price adjustments for offers which provide for lower Contracted percent ash and, as applicable, lower Contracted Half-Month SO2.

**	Half Month Suspension should be reasonably close to the contracted specification.

***	 Daily/Lot refers to each barge load of coal or at Buyer’s election a composite of two or more barges of coal   for barge deliveries or each unit train for rail deliveries.

8.	Type of Mine(s):  Surface _______%   Underground  _______%

9.	Mine District: _______________________________________________________________________________

10.	Name of Seam(s): ___________________________________________________________________________

11.  Preparation:   Crushed, run-of-mine   ______%           Washed   _______%

12.  Comments: 	________________________________________________________________________________

________________________________________________________________________________

________________________________________________________________________________

THIS IS A FIRM OFFER TO SUPPLY COAL UNDER ALL TERMS AND CONDITIONS INCLUDED IN THIS PROPOSAL PACKAGE, AND SHALL BE HELD OPEN BY SELLER FOR OPCO’S ACCEPTANCE THROUGH 5:00 P.M., WEDNESDAY, JANUARY 13, 2010.  UNTIL OPCO’S ACCEPTANCE HEREOF, WHICH SHALL BE AT ITS SOLE DISCRETION, THIS PROPOSAL SHALL NOT CONSTITUTE A VALID AND ENFORCEABLE AGREEMENT, BUT UPON OPCO'S ACCEPTANCE, SUCH PROPOSAL SHALL CONSTITUTE A VALID AND ENFORCEABLE AGREEMENT BETWEEN OPCO AND SELLER.

Proposal submitted by:

(Signature)

(Title)

(Company)

OHIO POWER COMPANY

OPCO RFP – LOW SULFUR PROPOSAL

RAIL TRANSPORTATION FACILITIES INFORMATION

The following information is required for each rail coal origin that is being bid:

Shipping Point_______________; Railroad(s)_______________; OPSL No. _______________

1)	What is the minimum and maximum unit train size that can be loaded?

2)	How fast can the indicated unit train be loaded?

3)	How precisely can the tonnage being loaded in each car be controlled?  What car loading precision would be guaranteed?

4)	Can the loading of the Unit Train start at any time and on any day upon the arrival of the cars?

5)	Is the assistance of the Railroad's locomotive and crew required to load the train?

6)	Are there any restrictions that would prevent your ability to load Buyer's 4,000 cubic feet AEPX hopper cars?

7)	How fast, after loading, can an advanced shipping manifest be FAXED to a location?

8)	Is equipment available for applying freeze-proofing and/or side release agents?

If there are any questions regarding this information being sought, please contact Jeff Dial at (614) 583-6972.

Signature

Title

Company

OHIO POWER COMPANY

OPCO RFP – LOW SULFUR PROPOSAL

BARGE TRANSPORTATION FACILITIES INFORMATION

The following information is required for each barge coal origin that is being bid:

Loading Dock

River Milepost

1)	What is the maximum number of Jumbo Barges that can be loaded in an eight-hour shift?

2)	How many shifts per day are barges loaded?

3)	How many days per week are barges loaded?

4)	How many loaded and empty Jumbo Barges can be accommodated in the harbor of the above named Loading Dock?

5)	Does this Loading Dock require the use of a harbor service for fleeting and switching?

6)	If the answer to #5 is Yes, please identify the required harbor service.

7)	Can the loading of barges commence at any time on any day upon arrival of the barges?

8)	How fast after loading can an advanced shipping manifest be FAXED to a location?

If there are any questions regarding this information being sought, please contact Jeff Dial at (614) 583-6972.

Signature

Title

Company

"DECLINE TO OFFER" FORM

TO AEP:  THIS FORM WILL SERVE AS OUR NOTICE TO YOU THAT WE ARE NOT SUBMITTING A PROPOSAL IN RESPONSE TO THIS CURRENT SOLICITATION.

PLEASE (CHECK ONE):   	( 	RETAIN US ON THE LIST FOR FUTURE SOLICITATIONS

( 	TAKE US OFF THE LIST FOR FUTURE SOLICITATIONS

COMPANY 	 	SIGNATURE

ADDRESS  	   	DATE

PHONE

RETURN BY:  January 6, 2010

  First Fold  

----------------------------------------------------------------------------------------------------------------------------------------------------------------Tape Here --

  Second Fold  

----------------------------------------------------------------------------------------------------------------------------------------------------------------

Place Postage Here

OPCO RFP – LOW SULFUR PROPOSAL

ATTN: JASON RUSK

AMERICAN ELECTRIC POWER SERVICE CORP.

155 W. NATIONWIDE BLVD.

SUITE 500

COLUMBUS OH  43215

# Text boxes

To access the blank Spot PO form, click on the box below: