April 19, 2011

The Fuel Procurement Department of the American Electric Power Service Corporation (“AEPSC”) is seeking bid proposals on behalf of one or more of its operating companies for the supply of coal to one or more power plants.  AEPSC may enter into one or more agreements, each for the supply of coal delivered by barge commencing as early as January 1, 2013.

Specifically sought are coals that: (1) have sulfur dioxide values (pounds SO2 per million Btu) and Chlorine (percent dry) meeting the requirements on the attached Coal Specification Table; and (2) meet the other quality specifications and supply parameters referenced on the attached Coal Specification Table.

The awarded contract(s) will be governed by the negotiated terms and conditions contained in the currently effective Master Coal Purchase and Sale Agreement (Master Agreement) between AEPSC and the successful bidder(s).  If the successful counterparty has not executed a Master Agreement with AEPSC, specifically negotiated terms and conditions mirroring those included in this solicitation will be executed as close as practicable.

AEPSC is seeking the following proposals:

- Term proposals which provides for up to 3.0 million tons of coal per year beginning in January 1, 2013 for 3 years;

- Term proposals which provides for up to 3.0 million tons of coal per year beginning in January 1, 2013 for up to 5 years (we will also consider extended terms);

The proposal(s) should include a stated price or prices for the relevant terms of the proposal(s) or a base price with proposed escalators.  Alternative pricing proposals will be considered.  Those offering coal are invited to submit their offers on one or more of the proposals and may make multiple offers on any proposal.

A completed  “Coal Proposal Form” shall comprise a “Coal Proposal Package”.  A copy of the Coal Proposal Form is contained herein.  In order to ensure that proposals are responsive to AEPSC’s needs and provide a uniform basis for evaluation, those providing offers are requested to complete a Coal Proposal Package for each submitted offer.  Typical coal analyses, including the Proximate, Ultimate, Trace Element and Mineral Ash Analyses; Grindability Index; and Ash Fusion Temperatures, should be submitted with the attached Coal Proposal Package.

The Coal Proposal Package(s), from a person having proper authority to legally obligate the bidder, along with any additional supporting material, must be received no later than 5:00 p.m., Monday, May 16, 2011.

Proposals are to be kept open for AEPSC’s acceptance until 5:00 p.m., Thursday, June 30, 2011.

All proposals are to be submitted by e-mail to coalrfp@aep.com, or by fax to (614) 583-1619 (Attention: Chuck West), or delivered in a sealed envelope marked "AEPSC ILLINOIS BASIN RFP - PROPOSAL" and addressed as follows:

AEPSC ILLINOIS BASIN RFP - Proposal

ATTN: Chuck West

American Electric Power Service Corp.

155 W. Nationwide Blvd.

Suite 500

Columbus  OH  43215

Proposals will be evaluated based upon the following factors:

- delivered cost (cents per million Btu),

- coal quality with appropriate price adjustments for guaranteed percent ash and pounds SO2 per million Btu

- reliability of supply and transportation flexibility

- terms and conditions

- previous experience with bidder and cooperation of bidding company in dealings with AEPSC

AEPSC reserves the right to modify or withdraw this invitation, to reject any or all proposals, and to terminate any subsequent negotiations at any time.  AEPSC also reserves the right to accept one or more proposal(s) for a portion or for all of the quantities of coal it seeks to acquire with this invitation.

AEPSC will consider every submitted offer on a confidential basis.

The bidder shall be responsible for the completeness and accuracy of all information contained in and used in preparation of its proposal(s) and for having supplied all necessary information.

If you do not wish to submit a proposal in response to this bid solicitation, please complete and return the attached, Decline to Offer form or send an e-mail to coalrfp@aep.com on or before Monday, May 16, 2011.  Failure to return this form or an e-mail indicating same, in lieu of submitting a proposal, may result in your removal from our bid list.

Should further information be required, please contact Chuck West, 614.583.6112 or Tina Sefcik, 614.583.6028.

Very truly yours,

Stephen M Debord

Vice President, Fuel Procurement

AMERICAN ELECTRIC POWER SERVICE CORPORATION

### COAL SPECIFICATION TABLE

| Specification “A” | Contracted | Applicable Lot (B)* |
| --- | --- | --- |
|  | Monthly (A)* | Rejection Limit |
|  |  | Minimum | Maximum |
| Calorific Value (Btu/lb.) | 11,000 | 10,200 | N/A |
| Sulfur Dioxide (lbs. SO2/MMBtu) (C)* | 5.00 | N/A | 6.20 |
| Moisture (%) | 11.00 | N/A | 13.00 |
| Ash (%) | 8.00 | N/A | 11.00 |
| Chlorine (% dry) | <0.20 | N/A | 0.20 |
| Hardgrove Grindability: | 45 | N/A | 40 |
| Ash Fusion Temp. (H=1/2W) ºF Red. | 2,250 | 2,000 | N/A |

N/A = Not Applicable

* Definitions:

(A) =  the half-monthly or monthly, as applicable, weighted average analysis result.

(B) = the analysis result of the sample (or composite of samples, if more than one) representing each unit train of coal.

(C) = For the purpose of determine the pounds of sulfur dioxide per million Btu, the figures shall be rounded to the nearest one hundredth.  For example, 4.954 pounds SO2/MMBtu shall mean 4.95 pounds SO2/MMBtu while 4.955 pounds SO2/MMBtu shall mean 4.96 pounds SO2/MMBtu and shall be deemed, for example, not to have met a 4.95 pounds SO2/MMBtu specification.

TERM COAL PROPOSAL FORM

DATE:

To:	 AEPSC ILLINOIS BASIN RFP - Proposal

ATTN: Chuck West

American Electric Power Service Corp.

155 W. Nationwide Blvd.

Suite 500

Columbus  OH  43215

Details concerning the supply of coal being offered herein to the American Electric Power Service Corp. are provided below:

1.  Seller(s):  (If Seller is a Sales Agent, include full names, addresses, and telephone numbers of Sales Agent and Producer and attach Producer's signed authorization for Sales Agent to “exclusively” make an offer on behalf of Producer.)

(a)  Seller(s):	(b)  Producer(s):

_________________________________	________________________________

_________________________________	________________________________

_________________________________	________________________________

_________________________________	________________________________

2.  Name(s) and location(s) of mine(s):  (Include name of mine operating company).

__________________________________________________________________________________

__________________________________________________________________________________

__________________________________________________________________________________

3.  MSHA ID _______________________________________________________________________

4.  Quantity offered (tons per year):  ___________________________________________________

5.  Term:  Up to five years; actual length of term shall be designated by AEPSC in the event of its acceptance.  Seller is to specify the earliest month coal is available:

__________________________________________________________________________________

6.  Shipping Point(s):

Barge Deliveries

Dock:  ______

River:

Milepost:  ____________________________

TERM COAL PROPOSAL FORM

AMERICAN ELECTRIC POWER SERVICE CORPORATION

FIXED PRICE SCHEDULE

3-Year Term Offer

Commencement Date           Year                      					Base Price per ton FOB “          ” prior to quality adjustments

Year 1 - 2013		$       .

Year 2 - 2014		$       .

Year 3 - 2015		$       .

Base Price Quality Adjustment:  In accordance with AEP’s standard Terms and Conditions

5-Year Term Offer *

Commencement Date           Year                      					Base Price per ton FOB “          ” prior to quality adjustments

Year 1 - 2013		$       .

Year 2 - 2014		$       .

Year 3 - 2015		$       .

Year 4 - 2016		$       .

Year 5 - 2017		$       .

* We will also consider extended terms

Base Price Quality Adjustment:  In accordance with AEP’s standard Terms and Conditions

TERM COAL PROPOSAL FORM

AMERICAN ELECTRIC POWER SERVICE CORPORATION

PRICE ADJUSTMENT SCHEDULE

(Based on Published Indices)

Initial Base Price per ton *

(2,000 lb. avoirdupois weight),

prior to quality adjustment

* Effective Date: __________								$             per ton FOB Barge

Base Price Adjustment:

Name and Number of U.S. Government

Description of				  Initial	 Amount	  	Bureau of Labor Statistics or other

Component of Price                  		  or % of Price	             	      Published Index

Fixed Component______________________		___________	Not Applicable_________________________

___________________________________		___________	_____________________________________

___________________________________		___________	_____________________________________

___________________________________		___________	_____________________________________

___________________________________		___________	_____________________________________

___________________________________		___________	_____________________________________

Government Assessment(s)           		___________	_____________________________________

*Base Price Per Ton

Prior to Quality

Adjustment			$___________

*At ___________ Btu per pound.

The applicable Base Price, which shall consist of the sum of the Adjustable Portion of Base Price and the Government Assessment(s) Portion of Base Price shall be redetermined, to the nearest tenth of a cent, on the dates designated and by the methods hereinafter prescribed.  The Base Price as so adjusted shall be the Base Price applicable to any coal loaded for shipment on and after the effective date of any such adjustment and shall remain in effect until the Base Price is again so adjusted.

Additional Comments:

TERM COAL PROPOSAL FORM

7.	The quality of Term coal being offered herein is intended to meet one of the following specifications as stated on the Coal Specification Table:  	 Product A	 Other

8.	Guaranteed coal specifications 		“As-Received”:

Contracted		  Applicable Lot** 								 Half-Month  		    Minimum/Maximum***

a)  Calorific Value (Btu per pound)    	___________ 		_____________   Minimum

b)  Total Moisture (%)                  		___________ 	 	_____________   Maximum

c)  *Ash (%)                             		___________ 		_____________   Maximum

d)  Volatile Matter (%)                 		___________ 		_____________   Minimum

e)  Grindability (Hardgrove Index)       	___________ 		_____________   Minimum

f)  Ash Fusion Temperature (H = 1/2 W), oF

in Reducing Atmosphere	         	___________ 		_____________   Minimum

g)  Chlorine (% dry)                 		___________  		_____________   Maximum

h)  *SO2 (lbs./MMBtu)              		___________		_____________   Maximum

i)  Hg Range - dry whole coal (ppm)	___________ Min	_____________   Max

j)  Coal Top Size    	                 		___________

*	Offer evaluations will include appropriate price adjustments for offers which provide for lower Contracted percent ash and, as applicable, lower Contracted Monthly SO2.

**	Applicable Lot refers to each barge of coal.

9.	Type of Mine(s):  Surface _______%   Underground  _______%    Other  _______%

10.	 Mine District:  ___________________________________________________________________

11.	 Name of Seam(s):  ________________________________________________________________

12.  Preparation:   Crushed, run-of-mine   ______%           Washed   _______%	Synfuel  ________%

13.  Comments:  ____________________________________________________________________

__________________________________________________________________________________________

THIS IS A FIRM OFFER TO SUPPLY FUEL UNDER ALL TERMS AND CONDITIONS INCLUDED IN THIS PROPOSAL PACKAGE, AND SHALL BE HELD OPEN BY SELLER FOR AEPSC’S ACCEPTANCE THROUGH 5:00 P.M., THURSDAY, JUNE 30, 2011 .  UNTIL AEPSC’S ACCEPTANCE HEREOF, WHICH SHALL BE AT ITS SOLE DISCRETION, THIS PROPOSAL SHALL NOT CONSTITUTE A VALID AND ENFORCEABLE AGREEMENT, BUT UPON AEPSC'S ACCEPTANCE, SUCH PROPOSAL SHALL CONSTITUTE A VALID AND ENFORCEABLE AGREEMENT BETWEEN AEPSC AND SELLER.

Proposal submitted by:

(Signature)

(Title)

(Company)

"DECLINE TO OFFER" FORM

TO AEP:  THIS FORM WILL SERVE AS OUR NOTICE TO YOU THAT WE ARE NOT SUBMITTING A PROPOSAL IN RESPONSE TO THIS CURRENT SOLICITATION.

PLEASE (CHECK ONE):   	( 	RETAIN US ON THE LIST FOR FUTURE SOLICITATIONS

( 	TAKE US OFF THE LIST FOR FUTURE SOLICITATIONS

COMPANY 	 	SIGNATURE

ADDRESS  	   	DATE

PHONE

RETURN BY:  May 16, 2011

  First Fold  

---------------------------------------------------------------------------------------------------------------------------------------------------------------Tape Here --

  Second Fold  

-------------------------------------------------------------------------------------------------------------------------------------------------

Place Postage Here

AEPSC ILLINOIS BASIN RFP

ATTN: CHUCK WEST

AMERICAN ELECTRIC POWER SERVICE CORP

155 W. NATIONWIDE BLVD.

SUITE 500

COLUMBUS OH  43215