March 18, 2010

INTRODUCTION

The Fuel, Emissions and Logistics group, on behalf of American Electric Power Service Corporation (AEPSC), is seeking proposals for the supply of coal to one or more power plants.  AEPSC may enter into one or more agreements, each for the supply of up to 150,000 tons of coal per month, delivered by rail or barge, commencing as early as July 2010.

The solicitation seeks coal that meets the specifications on the attached “Coal Specifications.” All proposals will have specifically negotiated terms and conditions, but will mirror those included in this solicitation as close as practicable.

AEPSC is seeking a proposal that provides for spot coal beginning July 2010 and ending December 2010 as well as January through December 2011.  AEPSC is also seeking a proposal that provides term coal beginning in January 2011 extending three to five years.  Additionally, AEPSC is in preparation for conducting one or more test burns of Illinois Basin (ILB) coal prior to December 2010.  Contingent upon the results of these tests, AEPSC may elect to procure ILB during the periods noted above.

Each valid proposal should include:

- The Seller’s and Producer’s name(s);

- The location of the mine;

- The mine type (surface or underground) ;

- The seam of coal being mined;

- The mine district;

- The quality of the coal, inclusive of suspension/rejection limits;

- The coal preparation (washed, crushed run-of-mine, etc.);

- The tons proposed for delivery each month;

- The stated price per ton;

- The commencement date and months of delivery;

- MSHA ID #’s, Environmental Permits, and the intended method of mining (mountain top removal, contour, or deep)

Proposals for rail-delivered coal will require: the rail origin station; the OPSL number; the number of railcars per shipment; the maximum loadout time; and the station’s ability to apply freeze control agent(s) and the listing of the agents.

COAL PROPOSAL PACKAGE

A "Spot Coal Proposal Form" if applicable, or a “Term Coal Proposal Form” and a "Rail Transportation Facilities Information" sheet, if applicable, or a "Barge Transportation Facilities Information" sheet, if applicable, shall comprise a “Coal Proposal Package.”  Copies of these forms are contained herein.  In order to ensure that proposals are responsive to AEPSC's needs, and that they provide a uniform basis for evaluation, any entity providing offers are required to complete a “Coal Proposal Package” for each submitted offer.  Typical coal analyses, including the Proximate, Ultimate, Trace Element and Mineral Ash Analyses, Grindability Index, and Ash Fusion Temperatures, shall be submitted with the attached “Coal Proposal Package.”

BID SUBMITTAL

The “Coal Proposal Package(s),” which should be signed by a person having proper authority to legally obligate the offering company, provided along with any additional supporting materials, must be received no later than 5:00 p.m., WEDNESDAY, MARCH 31, 2010.   Proposals are to be kept open for AEPSC's acceptance until 5:00 p.m., WEDNESDAY, APRIL 21, 2010.  All proposals are to be submitted by e-mail to coalrfp@aep.com, or by fax to (614) 583-1619 (Attention: Todd Adkins), or delivered in an envelope marked "AEPSC RFP - COAL PROPOSAL" and are to be addressed as follows:

AEPSC RFP – COAL PROPOSAL

ATTN:  TODD ADKINS, MANAGER, EASTERN FUEL PROCUREMENT

AMERICAN ELECTRIC POWER SERVICE CORP.

155 W. NATIONWIDE BLVD.

SUITE 500

COLUMBUS, OH  43215

If you do not wish to submit a proposal in response to this solicitation, please complete and return the attached "Decline To Offer" form on or before MARCH 31, 2010.

BID EVALUATION

Proposals will be evaluated based upon the following factors:

- Delivered cost (cents per million Btu);

- Coal quality with appropriate price adjustments for guaranteed percent ash and pounds SO2 per million Btu based on the relevant SO2 emissions allowances, inclusive of rejection limits;

- Reliability of supply and transportation flexibility;

- Terms and Conditions;

AEPSC reserves the right to modify or withdraw this invitation, to reject any or all proposals, and to terminate any subsequent negotiations at any time.  AEPSC also reserves the right to accept one or more proposal(s) for a portion or for all of the quantities of coal it seeks to acquire with this invitation.

AEPSC will consider every submitted offer on a confidential basis.

Those submitting proposals shall be responsible for the completeness and accuracy of all information contained in and used in preparation of its proposal(s) and for having supplied all necessary information.

All bid proposals shall be submitted by the Bidders at their sole cost and expense.

Should further information be required, please contact Todd Adkins at (614) 583-7452 or Denzil Welsh at (614) 583-7501.

Very truly yours,

James D. Henry

Vice President – Eastern Fuel Procurement

On behalf of American Electric Power Service Corporation

### COAL SPECIFICATIONS

Specification “A” (CSX Rail or NS Rail):

Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	12,500	12,350	< 12,200

Moisture (%)	  10.00	10.00	> 10.00

Ash (%)	12.00	12.50	> 12.50

Sulfur Dioxide (lbs SO2./mmBtu)	1.60	1.60	>   1.60

Specification “B” (CSX Rail or Barge):

Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	13,000	12,800	< 12,700

Moisture (%)	  7.00	8.00	>  9.50

Ash (%)	7.00	8.00	>  9.00

Sulfur Dioxide (lbs SO2./mmBtu)	2.60	2.80	>  3.05

Specification “C” (NS Rail or Barge):

Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	12,500	N/A	< 12,200

Moisture (%)	  7.00	8.00	> 10.00

Ash (%)	12.00	12.50	> 12.50

Sulfur Dioxide (lbs SO2./mmBtu)	1.05	1.05	>   1.05

Volatile Matter (%)	30.00	N/A	< 27.00

Hardgrove Grindability	50	N/A	<    48

Ash Fusion Temp. (H=½W)	  2700	N/A	  < 2450

Specification “D” (NS Rail):

Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	12,700	N/A	< 12,300

Moisture (%)	  7.00	8.00	> 10.00

Ash (%)	10.00	11.00	> 12.00

Sulfur Dioxide (lbs SO2./mmBtu)	1.60	1.60	> 1.65

Volatile Matter (%)	30.00	N/A	< 27.00

Hardgrove Grindability	60	N/A	< 55

Ash Fusion Temp. (H=½W)	  2700	N/A	< 2650

Specification “E” (Barge):

Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	12,000	11,900	< 11,800

Moisture (%)	  10.00	10.00	> 10.00

Ash (%)	13.00	13.50	> 13.50

Sulfur Dioxide (lbs SO2./mmBtu)	<1.60	1.60	> 1.60

Specification “F” (CSX Rail or Barge):

Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	12,500	12,350	< 12,200

Moisture (%)	  10.00	10.00	> 10.00

Ash (%)	9.00	10.00	> 11.00

Sulfur Dioxide (lbs SO2./mmBtu)	5.25	5.50	>  6.00

Specification “G” (Big Sandy Plant via Truck):

Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	12,000	11,900	< 11,800

Moisture (%)	  10.00	10.00	> 10.00

Ash (%)	12.00	12.00	> 12.50

Sulfur Dioxide (lbs SO2./mmBtu)	1.60	1.60	>  1.75

Specification “H” (ILB - Barge):

Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	11,500	11,400	< 11,400

Moisture (%)	  12.00	12.00	> 12.50

Ash (%)	8.00	8.00	>  9.00

Sulfur Dioxide (lbs SO2/mmBtu)	5.50	5.50	>  6.00

Chlorine (%)	0.18	0.18	>  0.18

Specification “I” (ILB - Barge):

Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	11,200	11,200	< 11,150

Moisture (%)	  12.00	12.00	> 12.50

Ash (%)	8.00	8.00	>  9.00

Sulfur Dioxide (lbs SO2/mmBtu)	4.50	5.50	>  6.00

Chlorine (%)	0.18	0.18	>  0.18

Specification “J” (PRB):

Contract 	      Half-Month         Daily/Lot Suspension/Reject

Calorific Value (Btu/lb)	8,800	8,800	< 8,500

Moisture (%)	  27.00	27.00	> 31.00

Ash (%)	5.00	7.00	>  7.50

Sulfur Dioxide (lbs SO2/mmBtu)	0.80	0.90	>  1.00

Sodium Oxide (%,As-Ignited)	1.00	1.00	>  1.00

The above contractual specifications may not exactly match one or more of the coal types a prospective supplier may have, but should be included in the one that most closely fits such specification.

Spot Coal Proposal Form

Page 1 of 6

SPOT COAL PROPOSAL FORM

DATE:

Details concerning the supply of coal being offered herein to the American Electric Power Service Corporation (AEPSC) are provided below:

| 1. Seller: (If Seller is a Sales Agent, include full names, addresses, and telephone numbers of Sales Agent and Producer and attach Producer's signed authorization for Sales Agent to “exclusively” make an offer on behalf of Producer.) |
| --- |
| (a) Seller: |  | (b) Producer: |
| 2. Name(s) and location(s) of mine(s): |
| 3. Quantity offered (tons per month): |  |
| 4. Term |  |
| (# years, beginning July, 2010; the actual length of Term shall be designated by AEPSC in the event of its acceptance of offer. Seller is to specify the earliest month coal is available). |
| 5. Bidder’s Shipping Point: |
| Rail Deliveries (minimum 90 cars) |
| Shipping Point(s): | Origin Station: |  |
|  | OPSL No. (Defined in OPSL 6000R): |  |
|  | No. of railcars/shipment* (>15): |  |
|  | Maximum Loadout Time: | 24 hrs. □ | 4 hrs. □ |

Spot Coal Proposal Form

Page 2 of 6

| Barge Deliveries |
| --- |
| Shipping Point(s): | Dock: |  |
|  | River: |  |
|  | Milepost: |  |
| 6. Pricing ($/short ton) | FOB Rail: |  |
|  | FOB Barge: |  |
| 7. Type of Mine(s): |
| Surface | % |  |
| Underground | % |  |
| 8. Mine District: |  |
| 9. Name of Seam(s): |  |
| 10. Preparation: |  |
| Crushed, run-of-mine | % |  |
| Washed | % |  |
| 11. Comments: |

Spot Coal Proposal Form

Page 3 of 6

- Guaranteed “Spot” coal specifications “As-Received”:

The quality of coal being offered herein is intended to meet one of the following specifications as stated on the Coal Specifications:

 Product A	 Product B		 Product C		 Product D		 Product E

 Product F		 Product G		 Product H		 Product I		 Product J

| Table 1 |
| --- |
| Parameter | Contracted Monthly Weighted Average Average | Suspension * | Rejection |
|  |  | Half-Month | Applicable Lot*** |
|  |  | Wtd. Avg | Wtd. Avg |
|  |  | minimum | maximum | minimum | maximum |
| Calorific Value (Btu/lb.) |  |  | N/A |  | N/A |
| Moisture (%) |  | N/A |  | N/A |  |
| Ash (%) |  | N/A |  | N/A |  |
| Volatile Matter (%) |  | N/A | N/A |  | N/A |
| Hardgrove Grindability |  | N/A | N/A |  | N/A |
| **Sulfur Dioxide (lbs. SO2 per mmBtu) |  | N/A |  | N/A |  |
| Ash Fusion Temp. (H=½W) oF Red. Atm. |  | N/A | N/A |  | N/A |
| **Ash Loading (lbs. Ash/mmBtu) |  | N/A |  | N/A |  |
| Sizing | 2” x 0 | N/A | N/A |  | 2.0” |

*  	Offer evaluations will include appropriate price adjustments for offers which provide for lower Contracted percent ash and, as applicable, lower Contracted Half-Month SO2.

**	Half Month Suspension should be reasonably close to the contracted specification.

***	Applicable Lot refers to each barge load of coal or at Buyer’s election a composite of two or more barges of coal   for barge deliveries or each unit train for rail deliveries.

Spot Coal Proposal Form

Page 4 of 6

THIS IS A FIRM OFFER TO SUPPLY COAL UNDER ALL TERMS AND CONDITIONS INCLUDED IN THIS COAL PROPOSAL PACKAGE, AND SHALL BE HELD OPEN BY SELLER FOR AEPSC’S ACCEPTANCE THROUGH 5:00 P.M., WEDNESDAY, APRIL 21, 2010.  UNTIL AEPSC’S ACCEPTANCE HEREOF, WHICH SHALL BE AT ITS SOLE DISCRETION, THIS PROPOSAL SHALL NOT CONSTITUTE A VALID AND ENFORCEABLE AGREEMENT, BUT UPON AEPSC'S ACCEPTANCE, SUCH PROPOSAL SHALL CONSTITUTE A VALID AND ENFORCEABLE AGREEMENT BETWEEN AEPSC AND SELLER.

Proposal submitted by:

(Signature)

(Title)

(Company)

Spot Coal Proposal Form

Page 5 of 6

Page 4 of 6

RAIL TRANSPORTATION FACILITIES INFORMATION

The following information is required for each rail coal origin that is being bid:

Shipping Point:								;

Railroad(s):								;

OPSL No.:								;

1)	What is the minimum and maximum unit train size that can be loaded?

2)	How fast can the indicated unit train be loaded?

3)	How precisely can the tonnage being loaded in each car be controlled?  What car loading precision would be guaranteed?

4)	Can the loading of the Unit Train start at any time and on any day upon the arrival of the cars?

5)	Is the assistance of the Railroad's locomotive and crew required to load the train?

6)	Are there any restrictions that would prevent your ability to load Buyer's 4,000 cubic feet AEPX hopper cars?

7)	How fast, after loading, can an advanced shipping manifest be FAXED to a location?

8)	Is equipment available for applying freeze-proofing and/or side release agents?

If there are any questions regarding this information being sought, please contact Jeff Dial at (614) 583-6972.

Signature

Title

Company

Spot Coal Proposal Form

Page 6 of 6

BARGE TRANSPORTATION FACILITIES INFORMATION

The following information is required for each barge coal origin that is being bid:

Loading Dock

River Milepost

1)	What is the maximum number of Jumbo Barges that can be loaded in an eight-hour shift?

2)	How many shifts per day are barges loaded?

3)	How many days per week are barges loaded?

4)	How many loaded and empty Jumbo Barges can be accommodated in the harbor of the above named Loading Dock?

5)	Does this Loading Dock require the use of a harbor service for fleeting and switching?

6)	If the answer to #5 is Yes, please identify the required harbor service.

7)	Can the loading of barges commence at any time on any day upon arrival of the barges?

8)	How fast after loading can an advanced shipping manifest be FAXED to a location?

If there are any questions regarding this information being sought, please contact Jeff Dial at (614) 583-6972.

Signature

Title

Company

Term Coal Proposal Form

Page 1 of 6

TERM COAL PROPOSAL FORM

DATE:

Details concerning the supply of coal being offered herein to the American Electric Power Service Corporation (AEPSC) are provided below:

| 1. Seller: (If Seller is a Sales Agent, include full names, addresses, and telephone numbers of Sales Agent and Producer and attach Producer's signed authorization for Sales Agent to “exclusively” make an offer on behalf of Producer.) |
| --- |
| (a) Seller: |  | (b) Producer: |
| 2. Name(s) and location(s) of mine(s): |
| 3. Quantity offered (tons per month): |  |
| 4. Term |  |
| (# years, beginning January, 2011; the actual length of Term shall be designated by AEPSC in the event of its acceptance of offer. Seller is to specify the earliest month coal is available). |
| 5. Bidder’s Shipping Point: |
| Rail Deliveries (minimum 90 cars) |
| Shipping Point(s): | Origin Station: |  |
|  | OPSL No. (Defined in OPSL 6000R): |  |
|  | No. of railcars/shipment* (>15): |  |
|  | Maximum Loadout Time: | 24 hrs. □ | 4 hrs. □ |

Term Coal Proposal Form

Page 2 of 6

| Barge Deliveries |
| --- |
| Shipping Point(s): | Dock: |  |
|  | River: |  |
|  | Milepost: |  |
| 6. Pricing ($/short ton) |  | FOB Rail |  | FOB Barge |
|  | Year 1: |  |  |  |
|  | Year 2: |  |  |  |
|  | Year 3: |  |  |  |
|  | Year 4: |  |  |  |
|  | Year 5: |  |  |  |
| 7. Type of Mine(s): |
| Surface | % |  |
| Underground | % |  |
| 8. Mine District: |  |
| 9. Name of Seam(s): |  |
| 10. Preparation: |  |
| Crushed, run-of-mine | % |  |
| Washed | % |  |
| 11. Comments: |

Term Coal Proposal Form

Page 3 of 6

TERM COAL PROPOSAL FORM

- Guaranteed “term” coal specifications “As-Received”:

The quality of coal being offered herein is intended to meet one of the following specifications as stated on the Coal Specifications:

 Product A	 Product B		 Product C		 Product D		 Product E

 Product F		 Product G		 Product H		 Product I		 Product J

| Table 1 |
| --- |
| Parameter | Contracted Monthly Weighted Average Average | Suspension * | Rejection |
|  |  | Half-Month | Applicable Lot*** |
|  |  | Wtd. Avg | Wtd. Avg |
|  |  | minimum | maximum | minimum | maximum |
| Calorific Value (Btu/lb.) |  |  | N/A |  | N/A |
| Moisture (%) |  | N/A |  | N/A |  |
| Ash (%) |  | N/A |  | N/A |  |
| Volatile Matter (%) |  | N/A | N/A |  | N/A |
| Hardgrove Grindability |  | N/A | N/A |  | N/A |
| **Sulfur Dioxide (lbs. SO2 per mmBtu) |  | N/A |  | N/A |  |
| Ash Fusion Temp. (H=½W) oF Red. Atm. |  | N/A | N/A |  | N/A |
| **Ash Loading (lbs. Ash/mmBtu) |  | N/A |  | N/A |  |
| Sizing | 2” x 0 | N/A | N/A |  | 2.0” |

*  	Offer evaluations will include appropriate price adjustments for offers which provide for lower Contracted percent ash and, as applicable, lower Contracted Half-Month SO2.

**	Half Month Suspension should be reasonably close to the contracted specification.

***	Applicable Lot refers to each barge load of coal or at Buyer’s election a composite of two or more barges of coal   for barge deliveries or each unit train for rail deliveries.

Term Coal Proposal Form

Page 4 of 6

RAIL TRANSPORTATION FACILITIES INFORMATION

The following information is required for each rail coal origin that is being bid:

Shipping Point:								;

Railroad(s):								;

OPSL No.:								;

1)	What is the minimum and maximum unit train size that can be loaded?

2)	How fast can the indicated unit train be loaded?

3)	How precisely can the tonnage being loaded in each car be controlled?  What car loading precision would be guaranteed?

4)	Can the loading of the Unit Train start at any time and on any day upon the arrival of the cars?

5)	Is the assistance of the Railroad's locomotive and crew required to load the train?

6)	Are there any restrictions that would prevent your ability to load Buyer's 4,000 cubic feet AEPX hopper cars?

7)	How fast, after loading, can an advanced shipping manifest be FAXED to a location?

8)	Is equipment available for applying freeze-proofing and/or side release agents?

If there are any questions regarding this information being sought, please contact Jeff Dial at (614) 583-6972.

Signature

Title

Company

Term Coal Proposal Form

Page 5 of 6

BARGE TRANSPORTATION FACILITIES INFORMATION

The following information is required for each barge coal origin that is being bid:

Loading Dock

River Milepost

1)	What is the maximum number of Jumbo Barges that can be loaded in an eight-hour shift?

2)	How many shifts per day are barges loaded?

3)	How many days per week are barges loaded?

4)	How many loaded and empty Jumbo Barges can be accommodated in the harbor of the above named Loading Dock?

5)	Does this Loading Dock require the use of a harbor service for fleeting and switching?

6)	If the answer to #5 is Yes, please identify the required harbor service.

7)	Can the loading of barges commence at any time on any day upon arrival of the barges?

8)	How fast after loading can an advanced shipping manifest be FAXED to a location?

If there are any questions regarding this information being sought, please contact Jeff Dial at (614) 583-6972.

Signature

Title

Company

Term Coal Proposal Form

Page 6 of 6

THIS IS A FIRM OFFER TO SUPPLY COAL UNDER ALL TERMS AND CONDITIONS INCLUDED IN THIS COAL PROPOSAL PACKAGE, AND SHALL BE HELD OPEN BY SELLER FOR AEPSC’S ACCEPTANCE THROUGH 5:00 P.M., WEDNESDAY, APRIL 21, 2010.  UNTIL AEPSC’S ACCEPTANCE HEREOF, WHICH SHALL BE AT ITS SOLE DISCRETION, THIS PROPOSAL SHALL NOT CONSTITUTE A VALID AND ENFORCEABLE AGREEMENT, BUT UPON AEPSC'S ACCEPTANCE, SUCH PROPOSAL SHALL CONSTITUTE A VALID AND ENFORCEABLE AGREEMENT BETWEEN AEPSC AND SELLER.

Proposal submitted by:

(Signature)

(Title)

(Company)

"DECLINE TO OFFER" FORM

TO AEP:  THIS FORM WILL SERVE AS OUR NOTICE TO YOU THAT WE ARE NOT SUBMITTING A PROPOSAL IN RESPONSE TO THIS CURRENT SOLICITATION.

PLEASE (CHECK ONE):   	( 	RETAIN US ON THE LIST FOR FUTURE SOLICITATIONS

( 	TAKE US OFF THE LIST FOR FUTURE SOLICITATIONS

COMPANY 	 	SIGNATURE

ADDRESS  	   	DATE

PHONE

RETURN BY:  March 31, 2010

  First Fold  

----------------------------------------------------------------------------------------------------------------------------------------------------------------Tape Here --

  Second Fold  

----------------------------------------------------------------------------------------------------------------------------------------------------------------

Place Postage Here

AEPSC RFP – COAL  PROPOSAL

ATTN:  TODD ADKINS, MANAGER, EASTERN FUEL PROCUREMENT

AMERICAN ELECTRIC POWER SERVICE CORP.

155 W. NATIONWIDE BLVD.

SUITE 500

COLUMBUS, OH  43215

# Text boxes

To access the blank Spot PO form, hold DOUBLE click on the link below: